## Slide 1: Project DELFT Digitizing Ethnological Films - an Expedition from Analogue to Digital
Miriam Reiche
No Time to Wait Conference, October 25-26, 2018

## Slide 2: DELFT: The Film Collection Institut for Scientific Film IWF
11.500 film titles
33.000 film copies
One of the world‘s largest collections of scientific films

## Slide 3: DELFT: The Ethnological Films of the Encyclopaedia Cinematographica
Founded in 1952 by Gotthard Wolf
Natural Sciences, Technology, Life Science, Medicine, Cultural Studies, Psychology

## Slide 4: DELFT: The Ethnological Films of the Encyclopaedia Cinematographica

## Slide 5: DELFT: Film Stock
  16mm Film copies (film base celluloseacetat, safetyfilm)
  black and white, colour
  silent films
  films with optical tracks
  SEPMAG, magnetic tape
  asynchronous audiotapes
  Digital Betacam
  additional material

## Slide 6: DELFT: Project Goals
Project Duration: October 2017-September 2019
Digitization of ca. 2000 film titles, approx. 500 hours of film
Cataloguing of the films
Making the films available via TIB‘s AV-Portal
Clarification of legal rights
Digital Object Identifier DOI for each film
Digital preservation

## Slide 7: DELFT: Process
Step 1: Selection of the film copy
Step 2: Choosing target format
Step 3: Digitizing
Step 4: Quality control
Step 5: Digital preservation

## Slide 8: Step 1: Film Copy Selection
Each digitizing project starts with the selection and description of the analogue object!
Filminspector RTI Pulsar
Selection of the film copy
Recording data for each film:
  Copy
  Mechanical damage
  Vinegar
  Shrinkage
  Colorfading

## Slide 9: Step 2: Target Formats 16mm Film
Original Format:
16mm Films positive black/white or color
Resolution: 2K
Sampling rate 10 bit
Color model and subsampling RGB 4:4:4
Frame rate: comparable to the original (16/18/24FPS)
Overscan
Target Format
Container: Matroska (.mkv)
VideoCodec: ffv1, Version 3 (GOP of 1, 16 Slices, CRC-Checksums per Slice)
Audio-Codec: linear PCM 96 kHz / 24 bit
Derivative Copy
Container: MPEG-4
Video Codec: H.264, CRF 20
Compression to 65%
original scanning resolution without scaling
4:3 aspect ratio
Audio Codec: AAC

## Slide 10: Step 2: Target Formats Digital Betacam
Original format: Digital Betacam black/white or color
Resolution: 720 x 576 Pixel
Framerate comparable to the original
Quantization/Bit: 10 bit
Color Space: Y′CBCR
Subsampling: 4:2:2
Master Interlaced
Derivative Progressive

## Slide 11: Step 3: Digitizing
Scanner: MWA Nova Spinner S
sprocketless and capstanless motion transport
unlimited shrinkage, warped film
large rollers for reduced stress on splices or brittle film
stable filmtransport
Warped film in the scanner

## Slide 12: Step 3: Digitizing
The scanner's diffuse light source reduces the effects of mechanical damage such as scratches etc.

## Slide 13: Step 4: Quality Control
→ 7 hours Film per Week → 2TB SSD Harddrive
Archival master ffv1/mkv
Derivative copy H.264/mp4 and H.265/mp4
Checksums framemd5
Technical metadata
Correct name of the file
Content completeness: film title, film duration
Image quality (artifacts etc.)
Playability of the master
File format validation
Policy alignment
Checksum check

## Slide 14: Step 5 Digital Preservation AV Material in the Digital Archive
Metadata: | 
Derivative Copy: | 
Preservation Master: | 
Metadata: | 
Derivative Copy: | 
Preservation Master: | ffv1/mkv
Metadata: | 
Derivative Copy: | H265/mp4
Preservation Master: | ffv1/mkv
Metadata: | descri
 | conservation MD (analogue film copy)
Derivative Copy: | H265/mp4
Collection: Projectnumber xyz (x films)
SIP Digitized Film | 
Preservation Master: | ffv1/mkv
Metadata: | descriptive MD
 | technical MD
 | conservation MD (analogue film copy)
Derivative Copy: | H265/mp4
SIP MAM Material | 
Preservation Master: | H264/mp4
 | supplementary material (booklet)
Metadata: | descriptive MD
Derivative Copy: | AdvancedVideo Codec/mp4 (for download)
SIP Project xyz Material | 
Preservation Master: | Project files photos descriptions etc.
SIP = Submission Information Package

## Slide 15: DELFT Experiences: Quality …an example: Digitizing 2007
Source material: 16mm - but which copy?
Resolution: SD and HD - but which film in which resolution?
Retouching, color correction - no documentation!
→ The digitization took place 20 years ago and we already have loss of information!

## Slide 16: DELFT Experiences: Definition of quality
Sustainability in the choice of digitization parameters
Collecting of standardized metadata
Documentation of the source material
Preservation of the originals
Retaining the authenticity of the original material

## Slide 17: DELFT Experiences: Retaining the authenticity of the original
mpeg1 (2007)
vob (2007)
mp4 (2018)
mp4 (2018)

## Slide 18: DELFT Experiences
Distribution copy 1
Archival copy
Distribution copy 2
Know your stuff !
The potential of a digital representation lies in the materiality of the analogue object; the technical possibilities help to transfer this potential.

## Slide 19: DELFT Experiences
  Additional materials contextualize the film!

## Slide 20: MORE INFORMATION: www.tib.eu TIB Digital Preservation: https://www.tib.eu/de/publizieren-archivieren/digitale-langzeitarchivierung/ Project DELFT: https://projects.tib.eu/delft/
Contact
Miriam Reiche
T +49 511 762-2587, Miriam.Reiche@tib.eu